Introduction

- Airplanes may be imported into Poland and used in OPS, provided it can be shown the airplane confirms to OPS-1 K &L sections

Purpose

- The intent of this compliance list is to ensure that an airplane to be operated under OPS-1 has been examined by the operator and is considered in conformity with the requirements of OPS-1

Applicability

- Import and dry lease-in of all airplanes used for commercial air transportation (CAT)

Reference

- This compliance list is derived from OPS-1

Completion of form

- Note 1: Each relevant box to be completed with a tick (() or a (X)

- Note 2: Add STC number (i.e. STC 12345-la)

- Note 3: Add reference of service publication and revision number or revision date (i.e. SB 25-1234, rev 2)

- Note 4: if Note 1, Note 2 and Note 3 not applicable, add references of other compliance documents (i.e. Mod 1234).  If OPS-1 paragraph is not applicable to airplane, complete column with’ Not applicable” (N/A)

| Requirement | Title | Method of Compliance |
| --- | --- | --- |
|  |  | Requirement satisfied through type design as specified In TCDS (Note 1) | Requirement satisfied through STC (Note 2) | Requirement satisfied through embodiment of manufacture service publications (Service Bulletins, Service changes, etc) (Note 3) | Other (Note 4) |
|  |  | YES | NO |  |  |  |
| 1.630 | General introduction |  |  |  |  |  |
| 1.630(a)(1) | Instruments and equipment: approved | ( | ( |  |  |  |
| 1.630(a)(2) | Operable condition | ( | ( |  |  |  |
| 1.630(b) | Instruments and equipment ETSO Or befor EU OPS as approved | ( | ( |  |  |  |
| 1.630(c) | Instruments and equipment: no equipment approval required: 1-10 | ( | ( |  |  |  |
| 1.630(d) | Equipment readily operable | ( | ( |  |  |  |
| 1.630(e) | Visibility of instruments | ( | ( |  |  |  |
| 1.635 | Circuit protection devices 10% spare fuses or min. 3 | ( | ( |  |  |  |
| 1.640 | Aeroplane operating lights | ( | ( |  |  |  |
| 1.640(a) | For flight by Day: |  |  |  |  |  |
| 1.640(a)(1) | Anti-colision light system | ( | ( |  |  |  |
| 1.640(a)(2) | Adequate illumination for All instruments & equipment essential to the safe operation | ( | ( |  |  |  |
| 1.640(a)(3) | Illumination in all pax compartments | ( | ( |  |  |  |
| 1.640(a)(4) | Electrical torch for each required crew member readily accessible | ( | ( |  |  |  |
| 1.640(b) | For flight by night: |  |  |  |  |  |
| 1.640(b)(1) | NAV/Pos. lights | ( | ( |  |  |  |
| 1.640(b)(2) | 2 landing lights or 1 with 2 sep. energy.filam. | ( | ( |  |  |  |
| 1.640(b)(3) | Collision light for seaplanes or amphibian | ( | ( |  |  |  |
| 1.645 | Windshield wipers | ( | ( |  |  |  |

| 1.650 | Day VFR operations – Flight and navigational instruments and associated equipment |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1.650(a) | Magnetic compass | ( | ( |  |  |  |
| 1.650(b) | Clock | ( | ( |  |  |  |
| 1.650(c) | Sensitive pressure altimeter | ( | ( |  |  |  |
| 1.650(d) | Airspeed indicator | ( | ( |  |  |  |
| 1.650(e) | Vertical speed indicator | ( | ( |  |  |  |
| 1.650(f) | Turn and slip indicator, or turn coordinator | ( | ( |  |  |  |
| 1.650(g) | Attitude indicator | ( | ( |  |  |  |
| 1.650(h) | Stabilized direction indicator | ( | ( |  |  |  |
| 1.650(i) | Outside temp. indicator ((C) | ( | ( |  |  |  |
| 1.650(j) | Equipment for flights<60 min, 50NM | ( | ( |  |  |  |
| 1.650(k) | Second pilot’s station: (2 pilots required) equipment according 1.650(c)-1.650(h) | ( | ( |  |  |  |
| 1.650(l) | Each airspeed indication systems must be with heated pitot tube | ( | ( |  |  |  |
| 1.650(l)(1) | Aeroplanes MTOM>5700kg or >9 pax | ( | ( |  |  |  |
| 1.650(l)(2) | Firs individual CofA after 1 april 1999 | ( | ( |  |  |  |
| 1.650(m) | Duplicate instruments required: Separate displays and selectors for each pilot | ( | ( |  |  |  |
| 1.650(n) | Means for indicating when power is not adequately supplied to the required flight instruments | ( | ( |  |  |  |
| 1.650(o) | Mach number indicator at each pilot/s station (A/C with compressibility limit) | ( | ( |  |  |  |
| 1.650(p) | Headset with Boom microphone or equivalent | ( | ( |  |  |  |
| 1.652 | IFR or night operations – Flight and navigational instruments and associated equipment |  |  |  |  |  |
| 1.652(a) | Magnetic compass | ( | ( |  |  |  |
| 1.652(b) | Clock (accurate, hours, min, sec) | ( | ( |  |  |  |
| 1.652(c) | Two sensitive pressure altimeter (feet) with counterdrum-pointer or equivalent presentation | ( | ( |  |  |  |
| 1.652(d) | Airspeed indicating system with heated pitot tube and indication of pitot heater failure (non required for A/C with 9 pax or less or MTOM<5700kg or issued with ind. CofA prior 1 April 1998) | ( | ( |  |  |  |
| 1.652(e) | Vertical speed indicator | ( | ( |  |  |  |
| 1.652(f) | Turn and slip indicator | ( | ( |  |  |  |
| 1.652(g) | Attitude indicator | ( | ( |  |  |  |
| 1.652(h) | Stabilized direction indicator | ( | ( |  |  |  |
| 1.652(i) | Outside temp. indicator ((C) | ( | ( |  |  |  |
| 1.652(j) | Two independent static pressure systems except that for propeller driven A/C with MTOM<5700 kg: 1 static and alternative | ( | ( |  |  |  |
| 1.652(k) | Second pilot’s station: (2 pilots required) equipment according 1.652(c)-1.652(h) | ( | ( |  |  |  |
| 1.652(l) | Aeroplanes MTOM>5700kg or >9 pax: additional standby attitude indicator (artificial horizon) useable by either pilot station, except MTOM<5700 kg registered in Member State on 1 April 1995 LH instrument panel acceptable | ( | ( |  |  |  |
| 1.652(l)(1) | After failure – powered from a source independent of normal electrical generating system | ( | ( |  |  |  |
| 1.652(l)(2) | Reliable operation for minimum of 30 min after total failure of normal electrical generating system | ( | ( |  |  |  |
| 1.652(l)(3) | Operates independently of any other attitude indicating system | ( | ( |  |  |  |
| 1.652(l)(4) | Operative automatically after total failure of the normal electrical generating system | ( | ( |  |  |  |
| 1.652(l)(5) | Appropriately illuminated during all phases of operation | ( | ( |  |  |  |
| 1.652(m) | Clearly evident to the flight crew when standby attitude indicator is being operated by emergency power | ( | ( |  |  |  |
| 1.652(n) | Illuminated chart holder | ( | ( |  |  |  |
| 1.652(o) | If installed Stby Attitude ind. Is certified acc CS25.1303(b)(4) or equivalent then only slip indicators are required | ( | ( |  |  |  |
| 1.652(p) | Whenever duplicate instruments required: separate displays and selectors for each pilots | ( | ( |  |  |  |
| 1.652(q) | Means for indicating when power is not adequately supplied to the required flight instruments | ( | ( |  |  |  |
| 1.652(r) | Mach number indicator at each pilot/s station (A/C with compressibility limit) | ( | ( |  |  |  |
| 1.652(s) | Headset with Boom microphone or equivalent for each flight crew on duty and transmit button on the control wheel | ( | ( |  |  |  |
| 1.655 | Additional equipment for single pilot operation under IFR or in a night: autopilot with at least altitude hold and heading mode | ( | ( |  |  |  |
| 1.660 | Altitude alerting system Turbine propeller Powered with MTOM>5700kg Or more than 9 pax seats Or turbojet Powered airplane Except: A/P with MTOM<5700kg and more than 9 pax, first CofA before 1.04.1972 and registered in a JAA member state on 01.04.1995 must be equipped with an altitude alerting system capable of: |  |  |  |  |  |
| 1.660(a)(1) | Alerting upon approaching preselected altitude and | ( | ( |  |  |  |
| 1.660(a)(2) | Alerting by at least an aural signal, when deviating above or below a preselected altitude | ( | ( |  |  |  |
| 1.665(a) | GPWS incl. TAWS (EGPWS): turbine powered airplane ant MTOM>5700kg or more than 9 seats | ( | ( |  |  |  |
| 1.665(b) | GPWS: Must be capable of at least sink rate, ground proximity, altitude loss after take off or go around, incorrect landing configuration and glide slope deviation | ( | ( |  |  |  |
| 1.665(c) | TAWS: Must provide visual and aural signals a terrain awareness display, with forward looking capability and terrain clearance floor | ( | ( |  |  |  |
| 1.668 | Airborne Collision Avoidance System turbine Powered airplane and MTOM>5700kgor >19 pax seat a min. performance level of at least ACAS II | ( | ( |  |  |  |
| 1.670(a)(1-2) | Airborne weather radar equipment: Pressurized A/P or unpressurized A/P with MTOM>5700kg or | ( | ( |  |  |  |
| 1.670(a)(3) | Unpres. A/P having more than 9 pax seats | ( | ( |  |  |  |
| 1.670(b) | Propeller driven pressurized A/P MTOM>5700kg or max pax seat<9, Airborne weather radar equipment | ( | ( |  |  |  |
| 1.675 | Equipment for operations in icing conditions |  |  |  |  |  |
| 1.675(a) | A/P certified to operate in icing conditions | ( | ( |  |  |  |
| 1.675(b) | At night; means to illuminate or detect the formation of ice (no glare or reflection) | ( | ( |  |  |  |
| 1.680 | Cosmic radiation detection equipment: applicable to airplanes to be operated above 49000ft (15000m) | ( | ( |  |  |  |
| 1.685 | Flight crew interphone system: including headsets and microphones, not of a handheld type | ( | ( |  |  |  |
| 1.690 | Crew member interphone system: |  |  |  |  |  |
| 1.690(a) | Required for airplanes with MTOM>15000 kg Or passenger seats >19 | ( | ( |  |  |  |
| 1.690(b) | Crew member interphone system must: | ( | ( |  |  |  |
| 1.690(b)(1) | Operate independently of the PA system except for handsets, headsets, microphones, selector switches and signaling devices | ( | ( |  |  |  |
| 1.690(b)(2) | Provide means of two-way com. between flight crew compartment and: | ( | ( |  |  |  |
| 1.690(b)(2)(i) | Each pax compartment | ( | ( |  |  |  |
| 1.690(b)(2)(ii) | Each galley located other than on pax deck level | ( | ( |  |  |  |
| 1.690(b)(2)(iii) | Each remote crew compartment not on the pax deck | ( | ( |  |  |  |
| 1.690(b)(3) | Be readily accessible from each crew stations in the flight crew compartment | ( | ( |  |  |  |
| 1.690(b)(4) | Be readily accessible at cabin crew member stations close to each separate or pair of floor level emergency exits | ( | ( |  |  |  |
| 1.690(b)(5) | Having an alerting system (aural or visual) | ( | ( |  |  |  |
| 1.690(b)(6) | Having a means to determine normal or emergency call | ( | ( |  |  |  |
| 1.690(b)(7) | Provide on ground: two-way comm.. between ground pers. And at least 2 flight crew members | ( | ( |  |  |  |
| 1.695 | Public address system |  |  |  |  |  |
| 1.695(a) | Required for airplane with pax seat>19 | ( | ( |  |  |  |
| 1.695(b) | The PA system must: | ( | ( |  |  |  |
| 1.695(b)(1) | Operate independently of the interphone system except for handsets, headsets, microphones, selector switches and signaling devices | ( | ( |  |  |  |
| 1.695(b)(2) | Be readily accessible from each required flight crew member station | ( | ( |  |  |  |
| 1.695(b)(3) | For each required floor level pax emergency exits with cabin crew seats: readily accessible microphone | ( | ( |  |  |  |
| 1.695(b)(4) | Be capable or operate within 10 sec | ( | ( |  |  |  |
| 1.695(b)(5) | Be audible and intelligible at all pax seats, toilets and cabin crew seats and work stations | ( | ( |  |  |  |
| 1.700 | Cockpit voice recorders – 1: more than 9 pax or MTOM>5700 kg first CofA after 1.04.1998 | ( | ( |  |  |  |
| 1.705 | Cockpit voice recorders – 2: MTOM<5700 kg >9 pax, first CofA 1.01.1990-31.03.1998 | ( | ( |  |  |  |
| 1.710 | Cockpit voice recorders – 3: MTOM>5700 kg, first CofA before 1.04.1998 | ( | ( |  |  |  |
| 1.715 | Flight data recorders – 1: more than 9 pax or MTOM>5700 kg, first CofA after 1.04.1998 | ( | ( |  |  |  |
| 1.720 | Flight data recorders – 2: MTOM>5700 kg, first CofA 1.06.1990-31.03.1998 | ( | ( |  |  |  |
| 1.725 | Flight data recorders – 3: MTOM>5700 kg, first CofA before 1.06.1990 | ( | ( |  |  |  |
| 1.727 | Combination Recorder | ( | ( |  |  |  |
| 1.730 | Seats, seat safety belts, harnesses and child restraint devices |  |  |  |  |  |
| 1.730(a)(1) | Seats or berths for each person | ( | ( |  |  |  |
| 1.730(a)(2) | Safety belt on each pax seat | ( | ( |  |  |  |
| 1.730(a)(3) | A child restraint device for each infant | ( | ( |  |  |  |
| 1.730(a)(4) | Safety belt with shoulder harness for each flight crew seat | ( | ( |  |  |  |
| 1.730(a)(5) | Safety belt with shoulder harness for each cabin crew seat | ( | ( |  |  |  |
| 1.730(a)(6) | Seats for cabin crew members located near required floor level emergency exits | ( | ( |  |  |  |
| 1.730(b) | Safety belts with shoulder harness must have a single point release | ( | ( |  |  |  |
| 1.730(c) | for A/P MTOM<5700 kg safety belts with diagonal shoulder strap or for A/P MTOM<2730 kg safety belt may be permitted in place of safety belt with shoulder harness | ( | ( |  |  |  |
| 1.731 | Fasten Seat Belt and No Smoking signs | ( | ( |  |  |  |
| 1.735 | Internal doors and curtains |  |  |  |  |  |
| 1.735(a) | Airplane with PAX seat>19: door between PAX Comp. and flight deck Comp. with placard “crew only” and locking means | ( | ( |  |  |  |
| 1.735(b) | Means (readily accessible) for opening each door that separates pax comp./other comp. that has emergency exit provisions | ( | ( |  |  |  |
| 1.735(c) | Door or curtain (separating pax cabin from areas with required emergency exit) must have a means to secure it in the open position | ( | ( |  |  |  |
| 1.735(d) | Placard (on door/adjacent to curtain – access to emergency exit) “Secured open during T/O and landing” | ( | ( |  |  |  |
| 1.735(e) | Means to unlock any door accessible to pax and can be locked by pax | ( | ( |  |  |  |
| 1.745 | First-Aid kits |  |  |  |  |  |
| 1.745(a) | Required number (dependent on pax) 0-99 # 1, 100-199 #2, 200-299 #3, >300 #4 | ( | ( |  |  |  |
| 1.745(b) | Period inspected, maintained, replenished | ( | ( |  |  |  |
| 1.755(a) | Emergency Medical Kit , more than 30 seats and 60 min flying time from medical assistance | ( | ( |  |  |  |
| 1.755(c)(1) | Dust and moisture proof, secure location | ( | ( |  |  |  |
| 1.755(c)(2) | Period. Inspected, maintained, replenished | ( | ( |  |  |  |
| 1.760 | First-Aid oxygen |  |  |  |  |  |
| 1.760(a) | Required for oper.alt>25000 ft, 3 litres, >8000 ft &<15000 ft 2%, no of dispensing units | ( | ( |  |  |  |
| 1.760(b) | Amount of first-aid oxygen | ( | ( |  |  |  |
| 1.760(c) | Mass flow 4l/min – 2l/min | ( | ( |  |  |  |
| 1.770 | Supplemental oxygen – pressurised aeroplanes |  |  |  |  |  |
| 1.770(a) (1)-(3) | General: above 1000 ft, calculation in accordance with emergency procedure in AFM, following cabin pressurization failure | ( | ( |  |  |  |
| 1.770(b) | Oxygen equipment and supply requirement | ( | ( |  |  |  |
| 1.770(b)(1) | Flight crew members, masks immediate reach, above 25000 ft quick donning mask | ( | ( |  |  |  |
| 1.770(b)(2) | Cabin crew members, additional crew members and passengers: Above or below 25000 ft Above 25000 ft – disp-units more than seats +10% Descent safely within 4 min to 13000 ft Automatically deploable oxyg.equipment | ( | ( |  |  |  |
| 1.775 | Supplemental oxygen – Non-pressurised aeroplanes |  |  |  |  |  |
| 1.775(a) 1, 2, 3 | General, above or below 10 000 ft, calculation: altitude, route emerg. - OM | ( | ( |  |  |  |
| 1.775(b) | oxygen supply requirements | ( | ( |  |  |  |
| 1.775(b)(1) | flight crew members | ( | ( |  |  |  |
| 1.775(b)(2) | cabin crew members, additional crew members and passengers | ( | ( |  |  |  |
| 1.780 | Crew Protective Breathing Equipment |  |  |  |  |  |
| 1.780(a) | required for pressurized A/P or unpressurized A/P with MTOM >5700kg or >19 seats - (15 Min.) | ( | ( |  |  |  |
| 1.780(b) | PBE easily accessible for immediate use by each req. flight crew member at their assigned duty station | ( | ( |  |  |  |
| 1.780(c) | PBE inst. adjacent to each required cabin crew member duty station | ( | ( |  |  |  |
| 1.780(d) | additional PBE located at or adjacent to the required hand fire extinguishers | ( | ( |  |  |  |
| 1.780(e) | PBE while in use must not prevent communication required by EU-OPS | ( | ( |  |  |  |
| 1.790 | Hand fire extinguishers |  |  |  |  |  |
| 1.790(a) | type and quantity of extinguishing agent | ( | ( |  |  |  |
| 1.790(b) | one Halon 1211 on the flight deck | ( | ( |  |  |  |
| 1.790(c) | one in each galley not located on the main passenger deck | ( | ( |  |  |  |
| 1.790(d) | one for each class A, B or E cargo comp. | ( | ( |  |  |  |
| 1.790(e) | required number in passenger comp. 7-30#1, 31-60#2, 61-200#3, +1/100Pax; | ( | ( |  |  |  |
| 1.790(f) | Halon 1211 requirement | ( | ( |  |  |  |
| 1.795(a) | Crash axes and crowbars >5700kg or >9Pax, located on flight deck | ( | ( |  |  |  |
| 1.795(b) | >200Pax one additional located most rear galley ,not visible to pax | ( | ( |  |  |  |
| 1.800 | Marking of break-in points | ( | ( |  |  |  |
| 1.805 | Means of emergency evacuation | ( | ( |  |  |  |
| 1.805(a) | required for exit sill heights >1.83m (6 ft) | ( | ( |  |  |  |
| 1.805(b) | requirem. for overwing emergency exits | ( | ( |  |  |  |
| 1.805(c) | requirem. for separate required flight crew exit | ( | ( |  |  |  |
| 1.810(a) | Megaphones seats 61-99, #1, 100 or more, #2 | ( | ( |  |  |  |
| 1.815 | Emergency lighting |  |  |  |  |  |
| 1.815(a) | required for aeropl. with >9 pax seats; independent power supply; | ( | ( |  |  |  |
| 1.815(a)(1) | requirem. for aeroplanes with >19 pax. | ( | ( |  |  |  |
| 1.815(a)(2) | requirem. for aeropl. (cert. to CS 23 or CS 25) with 19 or less pax. | ( | ( |  |  |  |
| 1.815(a)(3) | requirem. for aeropl. (not cert. to CS 23 or CS 25) with 19 or less pax. | ( | ( |  |  |  |
| 1.815(b) | requirem. for aeroplanes with 9 or less pax. | ( | ( |  |  |  |
| 1.820 | Emergency Locator Transmitter |  |  |  |  |  |
| 1.820(a) | Aircraft more than 19PAX 1.) One Automatic ELT or two ELT of any type 2.) CofA after 01-07-2008, Two ELTs – one Automatic | ( | ( |  |  |  |
| 1.820(b) | Aircraft 19Pax or less 1.) One ELT of any Type 2.) CofA after 01-07-2008, one Automatic ELT | ( | ( |  |  |  |
| 1.820(c) | Above ELTs shall comply with ICAO ANNEX 10, VOL III 406 MHz ELT | ( | ( |  |  |  |
| 1.825 | Life Jackets |  |  |  |  |  |
| 1.825(a) | requirem. for landplanes | ( | ( |  |  |  |
| 1.825(b) | requirem. for seaplanes and amphibians | ( | ( |  |  |  |
| 1.830(a) | Life-rafts and survival ELTs for extended overwater flights | ( | ( |  |  |  |
| 1.830(b) | sufficient life-rafts to carry all persons | ( | ( |  |  |  |
| 1.830(c) | at least two survival ELTs | ( | ( |  |  |  |
| 1.835 | Survival equipment | ( | ( |  |  |  |
| 1.835(a) | signaling equipment ( ICAO Annex 2) | ( | ( |  |  |  |
| 1.835(b) | at least one ELT | ( | ( |  |  |  |
| 1.835(c) | additional survival equipment | ( | ( |  |  |  |
| 1.840 | Seaplanes and amphibians – Miscellaneous equipment | ( | ( |  |  |  |
| 1.845 | General introduction |  |  |  |  |  |
| 1.845(a)(1) | communication and navigation equipment: approved and inst. | ( | ( |  |  |  |
| 1.845(a)(2) | installed such that the failure of any single unit will no result in the inability to communicate and/or navigate safely | ( | ( |  |  |  |
| 1.845(a)(3) | in operable condition, except in MEL | ( | ( |  |  |  |
| 1.845(a)(4) | equipment readily operable from ether pilot station | ( | ( |  |  |  |
| 1.845(b) | communication and navigation equipment: ETSO or before EU OPS as approved | ( | ( |  |  |  |
| 1.850 | Radio Equipment |  |  |  |  |  |
| 1.850(a) | equipped with radio required for the kind of operation | ( | ( |  |  |  |
| 1.850(b) | where two independent radio systems are required: independent antenna installation | ( | ( |  |  |  |
| 1.850(c) | radio communication equipment must also provide communications on 121.5 MHz | ( | ( |  |  |  |
| 1.855 | Audio Selector Panel | ( | ( |  |  |  |
| 1.860 | Radio equipment for operations under VFR over routes navigated by reference to visual landmarks requirements for radio equipment: |  |  |  |  |  |
| 1.860(a) | communicate with appropriate ground stations | ( | ( |  |  |  |
| 1.860(b) | communicate with appropriate air traffic control facilities | ( | ( |  |  |  |
| 1.860(c) | receive meteorological information | ( | ( |  |  |  |
| 1.865 | Communication and Navigation equipment for operations under IFR, or under VFR over routes not navigated by reference to visual landmarks required equipment: |  |  |  |  |  |
| 1.865(a) | Equipped with radio (communication and SSR transponder) and Navigation Equipment required by ATC. | ( | ( |  |  |  |
| 1.865(b) | Radio Equipment: Not less than: | ( | ( |  |  |  |
| 1.865(b)(1) | 2 independent radio comm. Systems necessary under normal operating conditions to communicate with appropriate ground stations from any point on the route including diversions, and | ( | ( |  |  |  |
| 1.865(b)(2) | SSR transponder as required for the route being flown. | ( | ( |  |  |  |
| 1.865(c) | for short-haul operations in the NAT MNPS airspace not crossing the North Atlantic, ONE long range COM system (HF-system) only if alternative COM procedures are published for the airspace concerned. | ( | ( |  |  |  |
| 1.865(d)(1) | Navigation equipment comprises not less than: | ( | ( |  |  |  |
| 1.865(d)(1)(i) | one VOR receiving system, one ADF system, one DME (except ADF carriage exception if ADF is not required) | ( | ( |  |  |  |
| 1.865(d)(1)(ii) | one ILS or MLS if req. | ( | ( |  |  |  |
| 1.865(d)(1)(iii) | one Marker Beacon receiving system if req. | ( | ( |  |  |  |
| 1.865(d)(1)(iv) | an Area Navigation System if req. | ( | ( |  |  |  |
| 1.865(d)(1)(v) | an additional DME system if req. | ( | ( |  |  |  |
| 1.865(d)(1)(vi) | an additional VOR receiving system if req. | ( | ( |  |  |  |
| 1.865(d)(1)(vii) | an additional ADF system if req. | ( | ( |  |  |  |
| 1.865(d)(2) | complies with R N P | ( | ( |  |  |  |
| 1.865(e) | alternative equipment, authorised by the Authority (addtl VOR / addtl ADF not requ.) | ( | ( |  |  |  |
| 1.865(f) | FOR IFR OPERATION: VHF COMs, VOR Receivers and ILS Localizers must be FM Immune acc ICAO ANNEX 10! | ( | ( |  |  |  |
| 1.865(g) | for ETOPS have a COM capable of communicating with an appropriate ground station. Beyond 180 min either voice based or data link. | ( | ( |  |  |  |
| 1.866(a)(1) | SSR Transponder with Mode C | ( | ( |  |  |  |
| 1.866(a)(2) | SSR Transponder with any other Mode required for the route being flown. | ( | ( |  |  |  |
| 1.870 | Additional navigation equipment for operations in MNPS airspace |  |  |  |  |  |
| 1.870(a) | navigation equipment according ICAO Doc 7030 | ( | ( |  |  |  |
| 1.870(b) | equipment visible and usable | ( | ( |  |  |  |
| 1.870(c) | for unrestricted operation in MNPS airspace: two independent LRNS | ( | ( |  |  |  |
| 1.870(d) | for operation in MNPS airspace along notified special routes: one LRNS | ( | ( |  |  |  |
| 1.872 | Equipment for operation in defined airspace with Reduced Vertical Separation Minima (RVSM) |  |  |  |  |  |
| 1.872(a)(1) | two independent altitude measurement Systems | ( | ( |  |  |  |
| 1.872(a)(2) | an altitude alerting system | ( | ( |  |  |  |
| 1.872(a)(3) | an automatic altitude control system | ( | ( |  |  |  |
| 1.872(a)(4) | a secondary SSR transponder with altitude reporting system that can be connected to AMS in use for altitude keeping | ( | ( |  |  |  |
| 1.873 | Electronic Navigation Data Management |  |  |  |  |  |
| 1.873(a) | Database Supplier NDB requires Type 2 LOA or equivalent. | ( | ( |  |  |  |
| 1.873(b) | If no Type 2 LoA or equivalent, the Authority has to approved operator’s procedures. | ( | ( |  |  |  |
| 1.873(c) | An operator shall not use electronic NDB products for other navigation applications unless the Authority has approved the operator’s procedures. | ( | ( |  |  |  |
| 1.873(d) | An operator shall continue to monitor both the process and the products according to the requirements of OPS 1.035 | ( | ( |  |  |  |
| 1.873(e) | Procedures for distribution and insertion of current and unaltered electronic navigation data. | ( | ( |  |  |  |
| I………………………………………Maintenance Manager/Accountable Manager (delete as applicable), certify that the above OPS 1 Compliance Statement is a true reflection of the equipment installed upon the aircraft to which it refers. |
| Signed ................................................... | Date ............................... |